## Slide 1: CSC485B Machine Learning for Robotics
SUNY Plattsburgh
Dr. Ned Lecky
Class 05- Getting Started with UR Programming

## Slide 2: Some Definitive Resources
YouTube: Hands-on
www.youtube.com/results?search_query=universal+robots+programming
UR Academy: Comprehensive
academy.universal-robots.com

## Slide 3: My Setup
Universal Robot UR-5e
All Robotics projects require some networking
UR Controller
Joint Controllers
Teach Pendant
Ethernet Switch
PoE Ethernet Switch
Security Cameras
My Laptop
VNC to Teach Pendant
Display Security Cams
Share to your screen!
120VAC Power

## Slide 4: Getting Started in 5 Minutes
Hardware: plug 3 things into the controller box
  Robot cable
  Teach pendant cable
  Power cord
Power On
  Press the silver button next to the E-Stop on the teach pendant
  Release E-stop by twisting it until it pops out
  System boots for a few minutes to here
Power off
  Press the silver button again while powered up
  You’ll get power off, restart, cancel options

## Slide 5: Enable the Robot
Release E-stop by twisting until it pops out
Click the Red Circle at the bottom left
Click ON
Click START
Brakes release and you’re on!
1
2
3

## Slide 6: Main Options at The Top
Run: Only allow existing programs to be loaded and used
Program: Create and modify programs
Installation: Setup features in the robot world
Move: Jog the robot around manually
I/O: Turn on and off digital/analog/serial/packet input/output
Log: View robot operation logs
Start here!
Try second!

## Slide 7: Jogging
TCP Position/Orientation
Tool Center Point (TCP)
  Try it in Feature: Base, Tool, and View
  (Move the view around to see the effect in View!)
Joint Position
  Moves one joint at a time
Freedrive
  Push and hold the button on the back of the teach pendant
  Can choose any set of axes to be free, in either base or tool coordinates

## Slide 8: Programming
Three sets of primitives
  Basic
  Advanced
  Templates
Optional 4th set
  URCaps (3rd party add-ons)
  Huge hardware and software ecosystem
  www.universal-robots.com/plus/products/?

## Slide 9: Things worth Demoing
Before we try an “application”
  TCP
  Payload/CG
  Free Drive
  MoveJ
  MoveL
  Direction Until
  URCap
  IO Control- look in the cabinet@
  About Robot Kinematics in Jog…
We’re using a UR here but you’d find all of these features and a fairly similar programming process for Fanuc, ABB, Kawasaki, Kuka, etc. etc. etc.
And always remember your Dress Pack!
  85% of all robot failures

## Slide 10: A First Program
Live Demo with the power supply!
Videos
  COMING SOON-ISH
So don’t forget UR Academy and YouTube!!