## Slide 1: CSC485B Machine Learning for Robotics
SUNY Plattsburgh
Dr. Ned Lecky
Class 09- Regression Wrap-Up

## Slide 2: Recall: Regression
Recall: regression is just taking one or more input variables and using them to predict one or more output variables (SISO, MISO, MIMO)
MUCH mathematical theory BUT
  The bulk of the theory assumes LINEAR equations
  Much theory also assumes that the input variables are independent
F
X
Y

## Slide 3: A Potential Architecture
You did this as Homework 2
VERY SMALL
MLP
side1
side2
side1^2
side2^2
hypotenuse^2
area
VERY SMALL MLP
side1
side2
hypotenuse
perimeter
y=sqrt(x)
hypotenuse^2
hypotenuse

## Slide 4: So Does This Have Any Practical Value
If it’s in this course, then HOPEFULLY!
So, an example?

## Slide 5: Back to Brighton Beach Lab
https://sites.google.com/lecky.com/brighton-beach-lab/home
The core problem: Plug Insertion
  The socket moves relative to the world
  The grasp of the plug in the gripper is unknown
  Exact alignment to << 1mm is required and that is at the limit of the robot
  Inspection just prior to insertion will be required to be successful

## Slide 6: Extracting Alignment Features
Used HALCON from MVTec

## Slide 7: BBL Theoretical Calibration
Compare theoretical calibration (by hand) with what LinearRegression comes up with
  https://sites.google.com/lecky.com/brighton-beach-lab/using-machine-learning/the-calibration-problem

## Slide 8: But it’s not accurate enough!
The relationships are close to linear but inputs are not independent!
An error of 1mm or 2 degrees makes insertion fail

## Slide 9: Other Issues
  We have variation we can’t really model
    Slightly non-linear
    Input variables not really independent
    Camera positions not dependable or permanent
    Lens-to-lens, position, robot-robot variations
      How good are lenses?
      https://www.edmundoptics.com/f/uc-series-fixed-focal-length-lenses/15027/
      Check out specs
      You even get variation based on light color!
  Easy to automate collection of a training dataset

## Slide 10: So… recommend auto calibration
Manually align connector to be “perfect”
Adjust, focus, lock-down all cameras
Run a robot program that offsets the connecter relative to perfect and acquires the measurement data
Now train something non-linear that doesn’t care much about input independence and you have a working calibration
AND: this process is automated and can be repeated at any time

## Slide 11: Summary
You need to understand your data
You need to design a process…
  Get data
  Scale it appropriately
  Augment inputs (maybe add x**2, or sin(x), or something you know will help)
  Partition the problem into pieces if you can
    Everyone likes end-to-end one-step ML because that looks cooler
      Rarely meets customer requirements
    (Log in to DMF???)

## Slide 12: A look at my solution
Small walkthrough, not really a requirement!
And a tiny intro to Keras/TensorFlow
  https://keras.io/

## Slide 13: A Real Dataset
One I’m suffering with right now
A large team in Poland is working on making this reliable right now
  Aurora Vision (formerly Adaptive Vision, now part of Zebra Technologies)
What makes things hard?
How else might we solve this problem (without ML/DL??)

## Slide 14: CSC485: Where Next?
Classification with ScikitLearn (instead of Regression)
And we can mix in Keras to use other techniques as we go, BUT
  If SciKit learn fails, you may do no better with “more” poorly thought-out ML! 